## Slide 1: Release the Kraken:
New KRACKs in the 802.11 Standard ACM SIGSAC Conference on Computer and Communications Security Toronto, Canada, 16 October 2018

## Slide 2
Mathy Vanhoef
Frank Piessens
Authors

## Slide 3
Former One by the Authors

## Slide 4
Outcomes of the titled paper
Generalize attacks against the 4-way handshake
Systematic investigation of 802.11 standards for key reinstallations vulnerabilities
Invention of more trickier approaches to trigger reinstallations attack
Investigation of effectiveness of official countermeasure of 802.11 and some patches
Seemingly innocent implementation bugs or protocol features can act as gadgets that enable exploitation of other vulnerabilities.

## Slide 5
Some jargons to fathom
802.11
Handshake
Temporal keys in WPA2
  PTK
  GTK
  IGTK
KRACK (Key Reinstallation AttaCKs)

## Slide 6
802.11
A set of technology standards for wireless network devices determined by the IEEE.
Main motivations of various standards 1.Data rate
2.Range

## Slide 7
Handshake

## Slide 8
Handshake

## Slide 9
Handshake

## Slide 10
Handshake

## Slide 11
Handshake

## Slide 12
Handshake

## Slide 13
Handshake

## Slide 14
Handshake

## Slide 15
Handshake

## Slide 16
Temporal keys WPA2
PTK : Pairwise Transient Key
Protects unicast communications between AP and client
Generated using EAPOL 4-way Handshake
  PTK = Function of (PMK,Nonce(Aonce), Nonce(Sonce), MAC Adr)
GTK : Group Transient Key
Protects broadcast/multicast communications from AP to clients
Transported from AP to client in EAPOL 4-way Handshake or Group 2-way Handshake
IGTK : Integrity Group Transient Key
Protects broadcast/multicast management frames (MFP)from AP to clients
Transported from AP to client in EAPOL 4-way Handshake or Group 2-way Handshake
Used for integrity check of broadcast/multicast management frames and is used to compute the MIC for Broadcast/multicast frames.

## Slide 17: Key reinstallations in the 4-way handshake

## Slide 18: WPA2: 4-way handshake
Used to connect to any protected Wi-Fi network
Negotiates fresh PTK: pairwise transient key
Mutual authentication

## Slide 19: WPA2: Encryption algorithm
Plaintext data
 Nonce reuse implies keystream reuse (in all WPA2 ciphers)
Nonce
PTK Mix
(session key)
Packet key
Mix
Flags | MAC Adr | Packet Number (PN) | Counters

## Slide 20
Peril of packet number reuse
So, if two packets P1 and P2 are encrypted with PTK, then
E1 = P1 KS1 E2 = P2 KS2
and if P1 and P2 were to use same Packet Number (PN), then KS1 = KS2
in that case, E1 E2 = P1 P2 [ Effect of encryption eliminated!! ]
So, if P1 is known/can be guessed, it is possible to Decrypt P2

## Slide 21: KRACK Attack

## Slide 22: KRACK Attack

## Slide 23: KRACK Attack
PTK = Combine(shared secret,
ANonce, SNonce)

## Slide 24
KRACK Attack

## Slide 25
KRACK Attack
Block Msg4

## Slide 26
KRACK Attack
Block Msg4

## Slide 27: KRACK Attack
PTK is installed & nonce set to zero
Block Msg4

## Slide 28: KRACK Attack

## Slide 29: KRACK Attack

## Slide 30
KRACK Attack
In practice Msg4 is sent encrypted

## Slide 31: KRACK Attack

## Slide 32
KRACK Attack
Key reinstallation: nonce again reset!

## Slide 33: KRACK Attack

## Slide 34
KRACK Attack
Next frame reuses previous nonce!

## Slide 35: KRACK Attack
Keystream

## Slide 36: KRACK Attack
Keystream
Decrypted!

## Slide 37: Practical Obstacles

## Slide 38: Rejected Msg3

## Slide 39
Rejected Msg3
Plaintext Msg3 rejected

## Slide 40
Rejected Msg3
Plaintext Msg3 rejected
Solution: generate encrypted Msg3

## Slide 50: Msg3 is now encrypted

## Slide 52
Flawed countermeasure

## Slide 53: 802.11’s official countermeasure
“When the Key, Address, Key Type, and Key ID parameters identify an existing key, the MAC shall not change the current transmitter TSC/PN/IPN counter or the receiver replay counter values associated with that key.”

## Slide 54: Bypassing 802.11’s countermeasure
Group key transported in two frames
› EAPOL-Key frames
› WNM-Sleep frames

## Slide 55: Bypassing 802.11’s countermeasure
Group key transported in two frames
› EAPOL-Key frames
› WNM-Sleep frames
We can mix these frames
› WNM-Sleep installs new key
› Then EAPOL-Key reinstall old key

## Slide 56: Bypassing 802.11’s countermeasure
Group key transported in two frames
› EAPOL-Key frames
› WNM-Sleep frames
We can mix these frames
› WNM-Sleep installs new key
› Then EAPOL-Key reinstall old key
 Can reinstall the group key, so Can replay the broadcast and multicast traffics

## Slide 57: Details are non-trivial
WNM & Group HS group HS & WNM
4-way HS & WNM

## Slide 58: Implementation Specific Flaws

## Slide 59: Can we replay Message 4?
› Yes, certain MediaTek Drivers accept replayed Msg4’s
› Used in 100+ devices  many vulnerable products
ASUS RT-AC51U
TP-Link RE370K

## Slide 60: Are PTK rekeys implemented properly?
Rekey is a new 4-way handshake
› Same messages exchanged as in initial 4-way handshake
› But new ANonce and SNonce is used
macOS:
› Patched default KRACK attack
› But reused the SNonce during a rekey
› SNonce reuse patched in macOS 10.13.3

## Slide 61: Exploiting macOS’s SNonce reuse
Adversary can replay old handshake
› Need to inject encrypted message 1
› Feasible under specific conditions
› Causes key reinstallation

## Slide 62: Other findings
› Vulnerability of First Initial Link Setup (FILS) and Tunneled direct-link setup PeerKey (TPK) handshakes to key reinstallation.
› Mac-serviced Data Unit (MSDU) frames can be abused to spoof the sender and destination frames.
› use of Quality of Service (QoS) by 802.11 can be abused to get improved MitM and Delaying Reinstalls.

## Slide 63: Conclusion
› They made attacks more practical
› Bypassed official countermeasure
› showed Handling group keys is hard
› suggested to Keep auditing devices & protocols!

## Slide 64: Thank you!
Questions?
krackattacks.com/followup.html